1) What is the purpose of using pull-up resistors in GPIO inputs, and how are they configured on the ATmega328 (internal and external)?

The purpose of a pull-up resistor is to prevent the state of a pin from randomly reading high or low. Instead it ensures that the default state of the input pin is always pulled towards high u unless there is a button that, when pressed and is also connected to ground, will cause it to read low.
This can be achieved externally by taking a resistor and connecting it to both the voltage and a switch which when in off state, ensures that the input connection is also connected to the voltage through a resistor. Or internally where there is a pull-up resistor mechanism built into the micro controller but has the same effect.

However to enable the pull-up resistor mechanism internally, it isn’t as simple as connecting a resistor to the voltage source and to the input pin through means of a switch or something like that. There is a built in mechanism that can be enabled via software that can do this for you but we need to understand how it works before we use it.

Basically to activate the pull up resistor, you would first need to write 0 into the data direction register for the corresponding bit and write 1 into that same port register for the bit to basically say “Hey let’s make the default state high”. The mechanism through which this works is the combination of an AND gate and a transistor that when activated connects the GPIO pin to a voltage source. The AND gate that takes the inverted value of the data direction register bit and the port bit as an input, and sends the resulting value to a transistor which will then activate and create a connection between the voltage source and the gpio pin. The transistor is only active if 0 is written to the data direction bit because the inverted value for this is 1, and if the port register bit for the pin is also 1, that outputs a value of 1 which activates the transistor.
2) Using GPIO and ATMega328p datasheet, design the embedded system to turn on LEDS using an external switch:

Part A)
- Design a circuit in the box below and describe your design.
  - One input switch
    - Switch 1(port B2) button pushed without floading – push button → logical high
  - Two LEDs with 220 Ohm
    - LED1(port B 0) – Logical High → led ON
    - LED 2(port B 1) – Logical High → led ON
Since the arduino maps directly to the ATMega328p, I’m going to use wokwi to design this hardware. Here is what know, input is bit 2 of port b and output is bit 0 and 1 of port b. So that would make PB0, PB1 the outputs and PB2 the input.

On the arduino nano , the D8 pin corresponds to PB0, D9 pin corresponds to PB1 and the D10 pin corresponds to PB2.
Let’s start by connecting the input. We know that when the button is pushed the input pin needs to be reading high. To achieve this, we can use a pulldown resistor connected to the button on the same side as the input pin and then connect the voltage source to the other side of the button. Here is a picture of the connections with d10 being the input pin which corresponds to pb2.

Next let’s handle the output. We need two leds, one connecting to d9 and the other to d8 which corresponds to pb1 and pb0 respectively. We then need a resistor for each connecting to ground. Here is the resulting circuit.

5) How do you configure the ATmega328 to trigger an interrupt on a falling edge for INT1 pin? Provide the register settings.

Part B)
In order to access the registers, such as DDRx or PORTx in Microcontroller, how to use the pointer and variable? Explain the principle of accessing registers in C using a pointer with example codes.

So each register such as any data direction register(DDRx) or Port Register(Portx) are have a specific address that we can use a pointer to point to. If we want to access the contents of a register, we just simply deference the pointer pointing to the address and it will have access to the contents of the register at the address that we are pointing to. Here is some example code written in c showing that we are pointing to the port b data direction register and then de-referencing it to change a specific bit in that register.

First we declare the pointer globally

Next we assign it to an address

Then we can modify the contents of the register at the register by dereferencing the pointer.
*portDDRB &= 0; //set all bits in the data direction register to 0

Part C)
Write a code (based on circuit design from 4.a): When the switch is pushed, LED1 is on and LED 2 is off; When switch 1 is released, LED1 is on, and LED 2 is off.
The code for the program is in the following wokwi link:

https://wokwi.com/projects/442584461353817089

[External Interrupt]
4) Describe how external interrupts work on the ATmega328 and list the available external interrupt pins.

How external interrupts are set up:
External interrupts can be triggered through two pins, INT0 or INT1 which corresponds to PD2 and PD3 respectively. Broadly speaking there are three steps set up an external interrupt. Step 1 is to configure how the interrupt will be triggered using the external interrupt control register. Step 2 is to then enable the external interrupt by setting the appropriate bit in the external interrupt mask register. Step 3 is to ensure that the I-bit on the status register is enabled. This ensures that interrupts are enabled on the device.

So let’s say you want to set up an external interrupt. The first thing to do is to configure how the interrupt will be triggered. This can be accomplished through the external interrupt control register. The external interrupt control register has 2 bits for INT1 to control how an external interrupt will be triggered and 2 bits for INT0 to configure how a external interrupt will be triggered. For INT1, the two bits responsible for sense are called ISC11 and ISC10 which correspond to be 3 and 2 of the external interrupt control register. If both are set to 0, a low level generates an interruption request. If IC11 is set to 0 and ISC10 is set to 1, any logical change generates an interrupt request. If ISC11 is set to 1 and ISC10 is set to 0, the falling edge will generate an interrupt request. If ISC11 and ISC10 are both set to 1, the rising edge of a pin will generate the interrupt request. Similarly, you can configure how INT0 will trigger a request by doing the same to ISC01, ISC00.

The next thing to do is to set the appropriate bit in the external interrupt mask register. Only bits 1 and 0 of the external interrupt mask register are used. Bit 1 corresponds to INT1 and bit 0 corresponds to INT 0. Let’s say you want to enable INT1 pin to trigger external interrupts, set bit 1 of the external interrupt mask register to 1.
Lastly ensure that the status register I-bit(bit 7) is set to 1 so that interrupts are enabled on the device.

How external interrupts work:
If the event triggering an input occurs(rising edge, falling edge, low level, or any change), a flag is set in the external interrupt flag register. Then the system checks if the I-status bit is enabled and interrupt is enabled for the pin in the external interrupt mask register. If so, the cpu suspends what it’s doing and starts executing the corresponding interrupt service routine. After it finishes, the program resumes where it left off. Lastly it is important to note that the interrupt service routine is defined by the user for the corresponding pin using the ISR macro which defines an interrupt service routine for a specific interrupt vector. If INT0_vect is supplied as an argument to ISR, then that is the code to execute when INT0 is triggered.

5) How do you configure the ATmega328 to trigger an interrupt on a falling edge for INT1 pin? Provide the register settings.

As mentioned in the previous question, we have 3 steps. First we need to set bits 3 and 2 of the external interrupt control register to 1 and 0 respectively since we want a falling edge to trigger the interrupt. Then we need to set the bit corresponding to the INT1 pin in the external interrupt mask register to 1. Lastly we need to ensure that we enable interrupts on the system by setting bit I (7th bit) to a value of 1 in the status register.
Here is some code I wrote to show this process in all three steps.